## Slide 1
Speech Intelligibility Index
ANSI S3.5

## Slide 2: SII calculation
Input variables
Equivalent speech spectrum level = speech spectrum level measured at the point corresponding to the center of the listener's head
  → power average over time of speech sound pressure level contained within a 1 Hz wide frequency band:
  → for each calculation method the standard provides speech spectra at 4 different levels (normal, raised, loud, shout)
Equivalent noise spectrum level = noise spectrum level measured at the point corresponding to the center of the listener's head
  → in absence of an external noise, assume the equivalent noise spectrum level is -50 dB for each frequency band
Equivalent hearing threshold = average threshold accross the group of ears of the listeners for whom the SII calculation is performed

## Slide 3: SII calculation
Python function integrated into the SQMetrics class
SQMetrics.sii_ansi(method, speech, noise, threshold)
Variables | Type | Description
method | string | Frequency band method used for the calculation. 4 choices: 'critical_bands', 'equal_critical_bands', 'third_octave_bands', 'octave_octave_bands'
speech | string / SQMetric object | Speech spectrum level as an SQMetric object if known, or a string to use the standard data: 'standard_normal_speech', 'standard_raised_speech', 'standard_loud_speech', 'standard_shout_speech'.
noise | SQMetric object / float | to be used as speech data or float. In case of a single value, it will be set on each frequency band. If None, it is set to -50 dB.
threshold | string | Hearing threshold. If 'standard', the threshold from Zwicker is used. If None, the threshold is set to 0.

## Slide 4: SII calculation
Compute from speech spectrum
Known speech
Noise set to 10dB
Zwicker hearing threshold
s = SQMetrics(x_speech, y_speech, domain='freq', sii_input='speech')
s.sii(method='third_octave_bands', noise=10, speech='standard_normal_speech', threshold='standard')
→ it is also possible to give an array for the noise, if the frequency axis differs, the bands data will be computed.

## Slide 5: SII calculation
Compute from noise spectrum
Normal speech level from the standard
Known noise
Zwicker hearing threshold
s = SQMetrics(x_noise, y_noise, domain='freq', sii_input='noise')
s.sii(method='third_octave_bands', speech='standard_normal_speech', threshold='standard')
→ it is also possible to give an array for the speech level. If the frequency axis differs, the bands data will be computed.